## Slide 1: How to explore a large scenario space of future power systems? A multi-perspective analysis for Germany
IEWT, 15th of February 2023, VIenna
Ulrich Frey1, Karl-Kiên Cao1, Thomas Breuer2, Manuel Wetzel1, Shima Sasanpour1, Jan Buschmann1, Kai von Krbek1 and Aileen Böhme3
3
1
2

## Slide 2: Exploring the Scenario Space
The state of the art
Decarbonized futures
Best case
Trend
Worst case

## Slide 3: Exploring the Scenario Space
The objective
Decarbonized futures
Point of interest
Scenarios: n = 3600

## Slide 4: MEthodology

## Slide 5: Three Main Challenges
Huge solving times
Which scenario assumptions?
Which evaluation perspective?

## Slide 6: Three Solutions
Solving times
Scenario Assumptions
Evaluation Perspective
Parallelization on Supercomputers
Scenario Generator
Model coupling

## Slide 7: Introducing a complex workflow
POIs
Instance Generator
REMix (.dmp)
LP Solver
PIPS-IPM++
Indicator Models
AMIRIS
Python Scripts
Scenario Generator
Preprocessing
Sampling
Raw Data
Postsolve
Scenario Result

## Slide 8: Generation of multiple model instances
 | P1 | P2 | Pn
P1 |  | -2 | 0
P2 | -2 |  | 1
Pn | 0 | 1 | 
Model inputs
Static
e.g. network topology
„Drivers“
e.g. costs, demand
Model instance
Model instance
Model instance
Model instances
mean
min
max
Automated sampling within provided bandwiths
Literature review
Truncated normal distribution
Pseudo- correlations
Notes: Cross impact balance analysis

## Slide 9: Assessment: 27 Scenario indicators1
1 Buschmann, J., von Krbek, K., Schimeczek, C. “Energy System Indicators”, doi: 10.23728/b2share.fe70b138419243c0817425a0d2d5ae32, 2022
Economic feasibility
Electricity price volatilities
Average electricity price
Profitability by technology
Policy instrument costs
Sustainability
Dispersion of VRE generation
Carbon dioxide emissions
Renewable Energy Penetration Index
Shannon-Wiener-Index
Security of supply
Expected Flexibility Shortfall
Grid-related curtailment
Energy Not Served
Energy self sufficiency rate
Exemplary Indicators | Direc-tion
RE-share | ↑
CO2-emissions | ↓
Geographical dispersion of VRE power generation | ?

## Slide 10: From indicators to Points-of-Interest
Good indicators = ±1 standard deviation to means of population
Scenarios with ≥ 15 “good” indicators => Points-of-Interest

## Slide 11: Results

## Slide 12: Results 1: Overall distribution of technologies over 3600 runs

## Slide 13: Results 2: Clustering scenario groups
Target: Identifying clusters of scenarios by indicators
2 methods:
  K-means (minimizes average Euclidian distance)
  K-medoids (minimizes pairwise dissimilarities)
Variation: Different number of indicators / inputs used to see if cluster numbers differ
Result: Yes, 2-5 clusters

## Slide 14: Results 2: Clustering scenario groups
C1: n = 1220, high RE-share
C2: n = 631, inbetween C1 & C3
C3: n = 136, high % of conventials
T-tests between POI / No-POI not sig.

## Slide 15: Results 3: How many scenarios do we need at all?

## Slide 16: Limitations & Outlook
Limitations
  Not very ambitious scenarios
  Still LP
  Power sector only
  Cluster number is not really stable
Outlook
  Open up parameter space for more ambitious scenarios
  Introduce new indicators
  Change grid resolution

## Slide 17: Conclusion
Motivation: The „possibility space“
Results: Best-performing scenarios
Method: Workflow on Supercomputers
How to explore a large scenario space of future power systems: A multi-perspective analysis for Germany

## Slide 18: Thank you!
ulrich.frey@dlr.de