## Slide 1: Modeling District Heating Supply Patterns in a Decarbonized EU-Wide Energy System in 2050
Ali Kök(1), Anna Billerbeck(2), Pia Manz(2), Lukas Kranzl(1), Marcus Hummel(3)
(1)TU Wien, (2)Fraunhofer ISI, (3)e-think
IEWT 2023

## Slide 2
2
Outline
IEWT 2023
Motivation and Research Question
Methodology
  Modeling chain
  Hotmaps Dispatch model
  Scenario design
Results
Conclusion
Next Steps

## Slide 3
3
Motivation and Objective
Motivation
District Heating (DH) supply of EU-27 is highly based on fossil fuels
Research Question
What are the cost-minimal decarbonized DH generation portfolios
  of EU-27 in 2050, considering:
    DH grid expansion,
    Availability of renewable energy source (RES) and industrial excess heat (IEH) potentials?
IEWT 2023
Source: https://irees.de/en/2020/11/11/district-heating-and-cooling-trend-en/

## Slide 4
4
Methodology
The modeling chain: Comprehensive modeling of DH Ecosystem
IEWT 2023
1. Building Stock
Modeled using INVERT/EE-Lab1
2. DH Expansion
Possible future DH areas are identified based on the distribution costs
3. RES Potential
4. DH Supply Dispatch
Modeled using the Renovation Effect tool of Hotmaps [1] and the DH expansion model of [2]
RES and IEH potentials are calculated and mapped with a high spatial resolution. Potentials are mapped with the possible DH areas [3]
DH areas are clustered into up to four groups for each MS [3]
Modeled using Hotmaps DH Dispatch module [4]
The cost-minimal DH supply dispatch is calculated for each cluster

## Slide 5
5
Methodology
The modeling chain: High geographical resolution
IEWT 2023
LAU regions
4 Clusters
LAU regions
LAU regions

## Slide 6
6
Methodology
The modeling chain: Comprehensive modeling of DH Ecosystem
IEWT 2023
Invert/EE-Lab
Breakdown to hectare level
DH-expansion
Clustering of potential DH areas
DH Dispatch
Aggregation of cluster results to NUTS 0
Database of existing DH grids
Analysis of RES potentials
Regionalisation of IEH potential
NUTS 0
Higher geographical resolution
Criteria for feasibility
Grid cost ceiling
Market share (Expansion costs)
Policies affecting renovations (type, rate)
Policies affecting change of supply system

## Slide 7
7
Methodology
Hotmaps Dispatch Model
IEWT 2023
Mixed-integer linear program
Minimizes (total costs - revenues)
Optimizes both investments and operation of technologies
Works on an hourly level
Efficiencies of heat pumps modeled as a function of source, flow, and return temperatures
  Fixed efficiencies for all other technologies
wiki.hotmaps.eu/en/CM-District-heating-supply-dispatch

## Slide 8
8
Methodology
Hotmaps Dispatch Model
Objective Function

## Slide 9
9
Methodology
Modeling heat pumps

## Slide 10
10
Methodology
Main Assumptions: 2050
IEWT 2023
Greenfield investment optimization  nothing exists at the beginning
  Pre-installed capacities for Waste to Energy (WtE) plants
RES and industrial excess heat potentials  upper limit for heat generation
Technoeconomic data based on the ENER/C1/2018-4941 project
  Country and size-specific
Energy carrier prices (incl. taxes and fees) and emission factors based on the ENER/C1/2019-481 project
  Hydrogen: country-specific, 148 €/MWh on average
  Electricity: hourly and country-specific, 127€/MWh on average
  Biomethane: country-specific, 108 €/MWh on average
Depreciation time = lifetime of plants
Interest rate = 2%
Biomass: 35 €/MWh, IEH: 10 €/MWh, and CO2 price: 500 €/tCO2
waste: 0 €/MWh  also 0 emission factor

## Slide 11
11
Methodology
Main Assumptions
IEWT 2023
Insert heat pump temperature sensitivities
Insert temperature sensitivity of geothermal potentials  the temperature thresholds?
Insert energy carrier prices in a table?  we have country-specific prices

## Slide 12
12
Methodology
Technologies
IEWT 2023
Natural gas boiler
Natural gas CHP
Biomass boiler
Biomass CHP
WtE CHP
Air source heat pump
River water & lake heat pump
Wastewater heat pump
Solar thermal
Industrial excess heat (direct)
Geothermal direct (hydrothermal)
Geothermal direct (petrothermal)
Hydrogen boiler
Hydrogen CHP
Biomethane boiler
Heat storage

## Slide 13
13
Methodology
Scenario Design: System Temperatures
IEWT 2023
Two main scenarios:
High temperature
  Flow temperature: 95-85°C
  Return temperature: 60°C
Low temperature
  Flow temperature: 65-55°C
  Return temperature: 30°C
Sensitivity:
  High geothermal investment cost  100% increase
Dispatch: has a direct impact only on heat pumps
Chart: DH Generation Potential in EU-27 [TWh] (preliminary) [3]
| Petrothermal | Hydrothermal | Wastewater | Rivers and lakes
low temp | 220810.6101 | 178225.6061 | 229439.8468 | 168411.2985
high temp | 69786.1498 | 75896.7357 | 178998.5918 | 139953.695
Indirect impact through potentials

## Slide 14
14
Results: EU-27
IEWT 2023
Heat Generation
Low temperature
High temperature
Chart: 
| EU
Air source HP | 203061.9003
River water & lake HP | 15869.8848
Waste water HP | 16759.0168
Industrial excess heat (direct) | 23592.0133
Geothermal direct (hydrothermal) | 172496.0318
Geothermal direct (petrothermal) | 112706.6107
Solar thermal | 46.1497
Biomethane Boiler | 1829.4768
Waste to energy CHP | 103644.8926
Biomass Boiler | 10524.4601
Biomass CHP | 32936.6098
Hydrogen CHP | 0
TWh
TWh
Moderate Geothermal Investment Cost
High Geothermal Investment Cost
TWh
TWh
Chart: 
| EU
Air source heat pump | 216069.424
River and lake heat pump | 300.6547
Waste water heat pump | 122105.5075
Industrial excess heat (direct) | 43196.2721
Hydrothermal (direct) | 73379.7438
Petrothermal (direct) | 57058.2866
Solar heating | 16.122
Biomethane Boiler | 1424.6311
Waste to energy CHP | 51644.1219
Biomass Boiler | 22490.4863
Biomass CHP | 143667.8955
Hydrogen CHP | 0
Chart: 
| EU
Air source HP | 313434.0085
River water & lake HP | 21609.3509
Waste water HP | 16702.092
Industrial excess heat (direct) | 23592.0133
Geothermal direct (hydrothermal) | 116008.7864
Geothermal direct (petrothermal) | 353.0723
Solar thermal | 12.2691
Biomethane Boiler | 1770.7364
Waste to energy CHP | 103644.8926
Biomass Boiler | 15913.4949
Biomass CHP | 80260.3685
Hydrogen CHP | 0
Chart: 
| EU
Air source heat pump | 255732.5693
River and lake heat pump | 300.6547
Waste water heat pump | 139255.6748
Industrial excess heat (direct) | 43196.2721
Hydrothermal (direct) | 61868.1069
Petrothermal (direct) | 1410.1126
Solar heating | 20.689
Biomethane Boiler | 1258.1794
Waste to energy CHP | 51644.1219
Biomass Boiler | 23370.322
Biomass CHP | 153279.3443
Hydrogen CHP | 0

## Slide 15
15
Results
IEWT 2023
Heat Generation
Low temperature
High temperature
Chart: 
| EU
Air source heat pump | 185951.8325
River and lake heat pump | 300.6547
Waste water heat pump | 100664.7264
Industrial excess heat (direct) | 43196.2721
Hydrothermal (direct) | 73379.7438
Petrothermal (direct) | 57058.2866
Solar heating | 51709.1906
Biomethane Boiler | 1761.631
Waste to energy CHP | 51644.1219
Biomass Boiler | 22490.4863
Biomass CHP | 143576.8948
Hydrogen CHP | 0
Chart: 
| EU
Air source HP | 203061.9003
River water & lake HP | 15869.8848
Waste water HP | 16759.0168
Industrial excess heat (direct) | 23592.0133
Geothermal direct (hydrothermal) | 172496.0318
Geothermal direct (petrothermal) | 112706.6107
Solar thermal | 46.1497
Biomethane Boiler | 1829.4768
Waste to energy CHP | 103644.8926
Biomass Boiler | 10524.4601
Biomass CHP | 32936.6098
Hydrogen CHP | 0
TWh
TWh
Moderate Geothermal Investment Cost
High Geothermal Investment Cost
Chart: 
| EU
Air source HP | 310824.3514
River water & lake HP | 21455.7685
Waste water HP | 16707.8394
Industrial excess heat (direct) | 23592.0133
Geothermal direct (hydrothermal) | 116008.7864
Geothermal direct (petrothermal) | 11.2935
Solar thermal | 3113.9673
Biomethane Boiler | 1788.3132
Waste to energy CHP | 103644.8926
Biomass Boiler | 15913.4949
Biomass CHP | 80260.3685
Hydrogen CHP | 0
Chart: 
| EU
Air source heat pump | 216393.6347
River and lake heat pump | 300.6547
Waste water heat pump | 119468.8993
Industrial excess heat (direct) | 43196.2721
Hydrothermal (direct) | 61868.1069
Petrothermal (direct) | 133.8282
Solar heating | 60493.6469
Biomethane Boiler | 1785.5175
Waste to energy CHP | 51644.1219
Biomass Boiler | 23370.322
Biomass CHP | 153077.6795
Hydrogen CHP | 0
TWh
TWh

## Slide 16
16
Results: EU-27
IEWT 2023
Low temperature
High temperature
Chart: Average LCOH [€/MWh]
| Air source HP | Biomethane Boiler | Industrial excess heat (direct) | Geothermal direct (hydrothermal) | Geothermal direct (petrothermal) | Hydrogen boiler | River water & lake HP | Solar thermal | Waste water HP | Biomass Boiler | Biomass CHP | Waste to energy CHP
 | 34.307 | 150.9423 | 26.1686 | 17.1182 | 28.1372 | 130.4167 | 31.9115 | 29.094 | 47.4001 | 49.1824 | 40.0705 | 14.1586
Chart: Average full load hours
| Air source HP | Biomethane Boiler | Industrial excess heat (direct) | Geothermal direct (hydrothermal) | Geothermal direct (petrothermal) | Hydrogen boiler | River water & lake HP | Solar thermal | Waste water HP | Biomass Boiler | Biomass CHP | Waste to energy CHP
 | 3934.5606 | 39.6026 | 1526.0688 | 7161.1042 | 8745.0324 | 66.799 | 3739.8229 | 1437 | 1593.8611 | 2761.7679 | 4159.7424 | 7446.5938
Levelized Cost of Heat Full Load Hours
Chart: Average LCOH [€/MWh]
| Air source HP | Biomethane Boiler | Industrial excess heat (direct) | Geothermal direct (hydrothermal) | Geothermal direct (petrothermal) | Hydrogen boiler | River water & lake HP | Solar thermal | Waste water HP | Biomass Boiler | Biomass CHP | Waste to energy CHP
 | 38.6632 | 162.8594 | 20.0041 | 17.0323 | 28.2235 | 138.6144 | 45.1874 | 30.1646 | 46.3791 | 45.8368 | 41.7222 | 18.5516
Chart: Average full load hours
| Air source HP | Biomethane Boiler | Industrial excess heat (direct) | Geothermal direct (hydrothermal) | Geothermal direct (petrothermal) | Hydrogen boiler | River water & lake HP | Solar thermal | Waste water HP | Biomass Boiler | Biomass CHP | Waste to energy CHP
 | 4828.614 | 35.4103 | 1526.058 | 7844.4219 | 8758.8202 | 61.625 | 1966 | 1469.7 | 2952.4638 | 3488.6316 | 5126.8281 | 7468.026

## Slide 17
17
Conclusions
IEWT 2023
Heat pumps and geothermal could play an important role in the decarbonisation of the European DH sector
Natural gas is phased out with a carbon price of 500€/tCO2
Clear impact of system temperatures on the DH supply mix
Heat pumps have a significant share in DH supply in all scenarios
  Air source HPs are relevant in both temperature scenarios
  Waste-water HPs play a more important role in high-temperature scenario
  River water & lake HPs only in low temperature scenario
Geothermal has the highest share in heat generation in the low-temperature scenario
  Geothermal might partly replace heat pumps in the low-temperature scenario
  Share reduced by more than 50% in case of high investment costs
    Petrothermal is not in the supply mix anymore
Biomass depends on policy choices regarding biomass allocation and stringency of sustainability criteria according to the Renewable Energy Directive

## Slide 18
18
Next steps
Sensitivity and MS-level in-depth analyses
IEWT 2023
Analyzing results in MS-level
Analyzing the exploitation of potentials
Sensitivities
  Carbon price / positive emission factor for waste
  Policies on electricity price: no/lower tax for heat pumps
  Price variations for biomass
  Which further parameter variations/sensitivities would you suggest?

## Slide 19
19
Thank you for your attention!
Questions?
koek@eeg.tuwien.ac.at
IEWT 2023

## Slide 20
20
References
IEWT 2023
[1] https://www.hotmaps.eu/
[2] Fallahnejad, M., Kranzl, L., & Hummel, M. (2022). District heating distribution grid costs: a comparison of two approaches. International Journal of Sustainable Energy Planning and Management, 34, 79–90. https://doi.org/10.54337/ijsepm.7013
[3] Manz, P., Billerbeck, A., Kök, A., Fallahnejad, M., Fleiter, T., Kranzl, L., Braungardt, S. (2023). Renewable and excess heat potentials for climate-neutral district heating in Europe: GIS and clustering algorithm based approach. To be submitted.
[4] https://github.com/tuw-eeg/hotmapsDispatch/tree/reshc_pathways